## Slide 1
Spectrum is a finite resource.
The government carves it into bands, writes the rules for each, and sells the empty ones.
We've mostly run out of empty.
radio spectrum, fully allocated
3.5–3.8 GHz · federal (DOE links)
That mid-band was federal-only for decades — now it's being auctioned to 5G.
LINDA — Live IQ Navigation and Display Application · Mustafa A. Omran · Mentors: Aric Sanders · Dan Kuester · NIST SURF 2026

## Slide 2
The whole question is one number: the guard band.
Federal / DOE link
5G base station
guard band
( empty spectrum )
frequency →
Too little → leakage knocks out federal links.
Too much → a public resource fenced off; billions left on the table.
NIST doesn't pick the number. It hands the people who do a measurement they can trust.
LINDA · NIST SURF 2026
2

## Slide 3
The catch: the antenna you measure with changes the answer.
OMNI reference
the same signals — reported weaker
DIRECTIONAL dish ( >30 dBi )
>30 dBi of gain — the same signals, brighter
Same signals, brighter on the dish. Measure with the omni and you underestimate what the real receiver feels — the optimistic, dangerous answer.
LINDA · NIST SURF 2026
3

## Slide 4
striqt turns two antennas and a radio into a measurement.
125 MS/s → real calibrated dBm
Y-factor calibration: measures the receiver's own noise temperature and corrects for it
13 measurements, 5 built for 5G
PSS / SSS correlation, SSB spectrogram, cyclic autocorrelation
Publication-grade figures
IEEE and NIST report styles ship in the repo — batch is a design choice
sensor-sweep spec.yaml → archive
one YAML, one command, an archive of exactly what was in the air
striqt — D. Kuester, NIST
A serious, real-time instrument — built for batch. It sees everything, and shows you none of it live.
LINDA · NIST SURF 2026
4

## Slide 5
In the field, you point it and walk away for a week.
100 ms
one recording
every 5 min
around the clock
~1 week
interference follows a 24-hour cycle — a short survey is unreliable, not just smaller
identical, flawless data
dish → the sky
dish → a wall
A loose cable, a dead front end, a quiet band — striqt archives them all as flawless. You find out when the week is gone. You're recording on faith.
LINDA · NIST SURF 2026
5

## Slide 6
LIVE DEMO
LINDA — the window striqt never had.
two antennas · one shared scale · verified against the hardware · any radio
orientation → the peak → change a setting → the form → AHAWI → a $-cheap radio
LINDA · NIST SURF 2026
Notes: Switch to the live app (running since before you walked in). Fallback: phone speed test → recorded clip.

## Slide 7
Watch the measurement — and trust it — on any radio.
Eyes
watch it live, and know you're recording what you meant to
Honesty
verified against the hardware; records into the group's archive with position
Anywhere
instrument-grade radio, or a two-orders-of-magnitude cheaper one
Before I handed it over: a 26-finding audit against my own system — every one fixed, each with a written test.
The same question is everywhere: CBRS vs. naval radar · 6 GHz Wi-Fi over utility microwave · radar altimeters.
It's running right now — the address is on the screen. This summer I built the thing that lets you watch that measurement, and trust it.
LINDA · NIST SURF 2026
7
Notes: Walk back to the cart and the live screen. Leave this up for Q&A — no 'Questions?' slide.