## Slide 1
Development of Visualization Frontends
for Cellular 5G-NR Measurements
Mustafa Omran · NIST SURF 2026
Applied Systems Metrology Group
Mentors: Aric Sanders, Dan Kuester

## Slide 2
NIST
SURF 2026
LINDA
THE RESOURCE
Spectrum is finite, and it is being sold.
3.5 to 3.8 GHz has been federal-only for a very long time.
Department of Energy point-to-point microwave links carry dam telemetry, reservoir levels and grid monitoring across terrain where fibre isn't realistic.
That same band is now being auctioned to carriers for 5G.
FEDERAL INCUMBENT
AUCTIONED · 5G
3.5 GHz
3.7
3.8 GHz
Neighbours, with nothing between them.
Selling a band works perfectly, as long as what you're selling isn't being used.
Notes: Beat: oil/minerals analogy, then the band, then the auction. Don't read the diagram.

## Slide 3
NIST
SURF 2026
LINDA
THE NUMBER
Too narrow breaks the link. Too wide burns billions.
A guard band is an empty strip of spectrum left between two competing users. You can be wrong in both directions.
TOO LITTLE
Leakage from the commercial side starts knocking out federal links. Dam telemetry, reservoir levels, grid monitoring.
TOO MUCH
A public resource is fenced off that nobody is allowed to use, and billions of dollars of auction revenue are left on the table.
NIST doesn't pick that number. NIST hands the people who do a measurement they can trust.
Notes: Land 'wrong in both directions'. The NIST line is the turn into the science.

## Slide 4
NIST
SURF 2026
LINDA
THE PROBLEM
The honest answer depends on which antenna you measure with.
OMNIDIRECTIONAL
What people normally measure with
Hears everything, from every direction, at once. A beam sweeping past is averaged in with the whole sky, so it barely registers.
HIGH-GAIN DISH
What you are actually protecting
Pointed at one thing, with more than 30 dBi of gain in that direction. The same beam arrives at full strength.
Same interference. Two completely different answers.
The omni's answer is the optimistic one. Which is the dangerous direction to be wrong in.
Notes: Pause before the red line. This is the thesis of the whole research programme.

## Slide 5
NIST
SURF 2026
LINDA
THE RIG
So the lab records both, at the same time, on one radio.
OMNI
reference
DISH
32-element array in the field
BANDPASS
filter
LNA
amplifier
DEEPWAVE
AIR8201B · 2 ch
striqt → LINDA
measure · watch
Two antennas, one radio, one clock. The whole point is that the two channels are measured at the same instant, so they can be compared.
The field rig uses a 32-element dipole array. A real dish at these frequencies is too big to move between rooftops.
Notes: Gesture at the cart, not the slide. The dish joke lands here.

## Slide 6
NIST
SURF 2026
LINDA
THE INSTRUMENT · striqt, by Dan Kuester
striqt turns raw IQ into calibrated, real-dBm measurement.
IQ
complex baseband, up to 125 MS/s
RESAMPLE
exact, in the frequency domain
CALIBRATE
Y-factor against a known noise source
ANALYSE
13 measurements, 5 of them 5G
ARCHIVE
labelled zarr, units on every axis
It refuses rather than approximate.
striqt searches for FFT sizes that make the rate ratio an exact rational number. If it can't find one, it raises instead of getting close.
Y-factor is what makes it metrology.
Measured against a noise source of known temperature, so you know how much of what you're seeing the radio added itself.
One command runs it: sensor-sweep spec.yaml → a calibrated archive.
Notes: Credit Dan by name and look at him. Don't read the pipeline boxes; narrate two of five.

## Slide 7
NIST
SURF 2026
LINDA
A clean recording doesn't mean you recorded what you meant to.
100 ms every 5 minutes, continuously, for about a week. You wheel the rig onto a roof, you point it, and you walk away.
A loose cable, a dead front end, an amplifier on backwards, or a band that simply had nothing in it — all four come back as a beautiful, clean archive. You find out at your desk, a week later.
Notes: Slowest slide in the deck. Let the headline sit before you speak.

## Slide 8
Live IQ Navigation and Display Application
Notes: Up before you speak. Don't read it. First words are the spectrum-as-a-resource line.

## Slide 9
LINDA
Live IQ Navigation and Display Application
Notes: Up before you speak. Don't read it. First words are the spectrum-as-a-resource line.

## Slide 10
LINDA
AHAWI
One coherent 100 ms capture. One striqt pass. Replayed 20 ms at a time.
100 ms is the recording length in the real field campaign. The 5G sync burst repeats every 20 ms, so each slice holds exactly one of them — and consecutive slices really are consecutive in time.
NIST
SURF 2026
Notes: Click 3, then cut back to the live view and scrub.

## Slide 11
NIST
SURF 2026
LINDA
PORTABILITY
Same software. Any radio.
Two commands to install. Plug a radio in and it works out what you gave it.
$20,000
Deepwave AIR8201B
Two receive channels. 125 MHz converter clock.
$2,000
Commodity SDR
One channel, over USB, on a Raspberry Pi.
git clone · bash install_linda.sh
Channel count and the list of sample rates the radio will actually accept come off the radio itself at startup. Nobody types them in.
Notes: This is the Gabe beat. Point at the second screen, not the slide.

## Slide 12
NIST
SURF 2026
The next person who puts one of these on a roof will know, in the first ten seconds, whether the week is going to be worth anything.
And not only 5G and dams.
Is this new signal going to step on that critical one? The question is everywhere right now.
CBRS
and naval radar
6 GHz Wi-Fi
over utility microwave
Radar altimeters
and 5G in C-band
striqt: Dan Kuester · Measurement framing: Aric Sanders · NIST Communications Technology Laboratory
LINDA
Notes: End here. Do not add a 'Questions?' slide. Stop talking after 'worth anything'.